## Slide 1: Springworks Farm Study # 2
Windham Packaging, LLC
Gabriela Hernandez

## Slide 2: Summary and Conclusions
Weight loss was negligible in all samples (<0.01%) throughout the entire study
There were no major quality differences between samples kept inside the cartons and outside the cartons suggesting that the amount of venting in the cartons was adequate to get cooling.
There was a significant amount of tip burn present in the inner leaves of both the romaine and green leaf.
  Tip burn in inner leaves is caused by calcium deficiency during growth and cannot be controlled by MAP.
  Tip burn in outer leaves is caused by environmental factors during growth (i.e. insufficient water supply or too much salt near the roots)
Tip burn in inner (left) and outer leaf (right)

## Slide 3: Summary and Conclusions
There was noticeably less browning in the stem during this study than the previous study, even in the green leaf samples kept in the Old OTR sleeves. Because there were no differences in the process, this can be attributed to natural variation in the pinking/browning enzyme. In the next study, a mixture of ascorbic and citric acid should be sprayed onto the butt end of the green leaf and baby romaine heads to see if browning is controlled.
The new OTR in the green leaf sleeves succeeded in extending shelf life. With these sleeves, we can achieve a shelf life of 17-19 days.
OTR1 (no perforations) caused anaerobic atmospheres inside the baby romaine bags and all samples were rotted before day 10. This is not a suitable bag for baby romaine.
Baby romaine OTR2 bags were more successful and extended shelf life to 14 days. We believe a higher O2 flux will further extend shelf life.
Additional testing should be done on the baby romaine comparing two different higher OTR bags.

## Slide 4: Results and Discussion:
Internal Temperature
Visual Quality Throughout Shelf Life
  Photos
  Visual Comparisons and Presence of Defects among Samples
Shelf Life Studies

## Slide 5: Internal Temperature – Green Leaf
Days in Storage | Product | Temperature Inside Bag (°F) | Temperature out of bag (°F)
7 | Green Leaf out of Carton - New OTR | 54.1 | 57.9
7 | Green Leaf out of Carton - Old OTR | 53.6 | 55.4
7 | Green Leaf in Carton - Old OTR | 54.9 | 55.9
7 | Green Leaf in Carton - New OTR | 53.6 | 55.8
10 | Green Leaf out of Carton - New OTR | 49.3 | 55.0
10 | Green Leaf out of Carton - Old OTR | 50.2 | Not Tested
10 | Green Leaf in Carton - Old OTR | 53.8 | 54.3
10 | Green Leaf in Carton - New OTR | 53.8 | 52.7
14 | Green Leaf out of Carton - New OTR | 48.2 | 52.7
14 | Green Leaf out of Carton - Old OTR | 49.5 | 50.7
14 | Green Leaf in Carton - Old OTR | 51.6 | 50.0
14 | Green Leaf in Carton - New OTR | 49.6 | 51.6
17 | Green Leaf out of Carton - New OTR | 46.8 | 52.5
17 | Green Leaf out of Carton - Old OTR | 45.7 | 50.9
17 | Green Leaf in Carton - Old OTR | 52.2 | 51.1
17 | Green Leaf in Carton - New OTR | 50.4 | 48.7
20 | Green Leaf in Carton - Old OTR | 60.2 | 55.9
20 | Green Leaf out of Carton - New OTR | 57.6 | 52.9

## Slide 6: Internal Temperature – Baby Romaine
Days in Storage | Product | Temperature Inside Bag (°F) | Temperature out of bag (°F)
7 | Baby Romaine out of Carton - OTR 1 | 57.4 | 57.2
7 | Baby Romaine out of Carton - OTR 2 | 59.4 | 55.9
7 | Baby Romaine in Carton - OTR 1 | 57.7 | 55.4
7 | Baby Romaine in Carton - OTR 2 | 56.5 | 54.9
10 | Baby Romaine out of Carton - OTR 1 | 57.6 | 53.4
10 | Baby Romaine out of Carton - OTR 2 | 57.4 | 54.9
10 | Baby Romaine in Carton - OTR 1 | 57.2 | 51.3
10 | Baby Romaine in Carton - OTR 2 | 55.0 | 48.4
14 | Baby Romaine out of Carton - OTR 1 | 54.1 | 50.7
14 | Baby Romaine out of Carton - OTR 2 | 54.1 | 51.8
14 | Baby Romaine in Carton - OTR 1 | 52.5 | Not Tested
14 | Baby Romaine in Carton - OTR 2 | 53.8 | 48.6
17 | Baby Romaine out of Carton - OTR 2 | 52.9 | 50.9
17 | Baby Romaine in Carton - OTR 2 | 56.5 | 48.4

## Slide 7: Headspace Levels in Green Leaf
Green leaf heads packaged in new OTR sleeves had slightly reduced O2 and increased CO2 compared to the old sleeves
  Reduced O2 and increased CO2 is known to extend shelf life in leafy greens. In this case, we believe that CO2 played a bigger role in extending shelf life because O2 levels in both OTR sleeves were very similar.
Average O2 was slightly lower and CO2 was higher when New OTR bags were placed inside the carton compared to outside the carton
  Less oxygen was circulated inside the cartons, which is expected. However, it did not make a difference in quality.
Chart: Headspace Gas in Green Leaf Sleeves
| Green Leaf in Carton | Green Leaf out of Carton | Green Leaf in Carton | Green Leaf out of Carton | Green Leaf in Carton | Green Leaf out of Carton | Green Leaf in Carton | Green Leaf out of Carton | Green Leaf out of Carton | 7 | 7 | 10 | 10 | 14 | 14 | 17 | 17 | 20
New OTR Sleeve | 17.1 | 18.4 | 19.5 | 19.7 | 18.9 | 19.15 | 18.8 | 19.4 | 19.55
Old OTR Sleeve | 18.3 | 19.4 | 20.2 | 20 | 19.8 | 19.4 | 19.8 | 19.9 | 20.35
Chart: 
| Green Leaf in Carton | Green Leaf out of Carton | Green Leaf in Carton | Green Leaf out of Carton | Green Leaf in Carton | Green Leaf out of Carton | Green Leaf in Carton | Green Leaf out of Carton | Green Leaf out of Carton | 7 | 7 | 10 | 10 | 14 | 14 | 17 | 17 | 20
New OTR SLeeve | 3.4 | 2.25 | 1.65 | 1.4 | 1.65 | 1.25 | 1.8 | 1.15 | 1.3
Old OTR Sleeve | 2.1 | 1.2 | 0.7 | 1.1 | 0.5 | 1 | 0.8 | 0.5 | 0.45

## Slide 8: Headspace Levels in Baby Romaine
Anaerobic conditions developed in OTR1 bags.
  Anaerobic atmospheres (~0% O2) are undesirable because they can result in early decay, off odors, and growth of harmful bacteria
  Baby romaine bags need to have higher OTRs to avoid these conditions
O2 in OTR2 bags fluctuated between 6 and 9%. This is due to normal changes in respiration during storage
CO2 in OTR2 bags was significantly lower than OTR1 bags. The elevated CO2 can help reduce red color development on the butt ends. However, too much CO2 accumulation can lead to injury and premature decay.
Chart: Headspace Gas in Baby Romaine Bags
| Baby Romaine out of Carton | Baby Romaine in Carton | Baby Romaine out of Carton | Baby Romaine in Carton | Baby Romaine out of Carton | Baby Romaine in Carton | Baby Romaine out of Carton | Baby Romaine in Carton | 7 | 7 | 10 | 10 | 14 | 14 | 17 | 17
OTR 1 Bag | 0.13333 | 0.2 | 0.16667 | 0.26667 | 0.2 | 0.2
OTR 2 Bag | 6.1 | 7.5333 | 7.35 | 9.1 | 6.1667 | 9.0667 | 6.25 | 7
Chart: 
| Baby Romaine out of Carton | Baby Romaine in Carton | Baby Romaine out of Carton | Baby Romaine in Carton | Baby Romaine out of Carton | Baby Romaine in Carton | Baby Romaine out of Carton | Baby Romaine in Carton | 7 | 7 | 10 | 10 | 14 | 14 | 17 | 17
OTR 1 Bag | 26.5667 | 21.4667 | 35.9667 | 28.1 | 36.9 | 33.1
OTR 2 Bag | 14 | 12.8667 | 14.3 | 11.9 | 16.3667 | 12.6667 | 16.05 | 14

## Slide 9: Visual Quality and Taste
Initial quality:
Green leaf
  Leaves were green and crisp with no signs of mildew.
  No tip burn visible
  No spotting or wilting
  Taste was fresh, no smell
Baby Romaine
  Leaves were green and crisp
  No signs of mildew
  Slight tip burn on a couple of exterior leaves
  Taste is fresh
Initial Green Leaf (top) and Baby Romaine (bottom)

## Slide 10: Day 7
Green Leaf
Both green leaf samples had red/brown stems and some brown lesions near the stems
Taste was good, texture was crisp
Baby Romaine
No difference in visual quality between OTR1 and OTR2 bags
Some mold present in outer leaves and browning in ribs near the stems
Some rust spots began to form
Taste was good and fresh. Texture was crisp

## Slide 11
Day 7 Green Leaf in Old OTR Bag – out of Carton
Day 7 Green Leaf in Old OTR Bag – inside Carton
Day 7 Green Leaf in New OTR Bag – out of Carton
Day 7 Green Leaf in New OTR Bag – inside Carton

## Slide 12
Day 7 Baby Romaine in OTR1 Bag – out of Carton
Day 7 Baby Romaine in OTR1 Bag – inside Carton

## Slide 13
Day 7 Baby Romaine in OTR2 Bag – out of Carton
Day 7 Baby Romaine in OTR2 Bag – inside Carton

## Slide 14: Day 10
Green Leaf
New OTR Sleeves:
  Some rust spots in outer leaves
  Taste was good; fresh
Old OTR Sleeves:
  1 outer leaf had severe rust spots and decay
  2 outer leaves had minor rust spots
  Taste was good; fresh
Baby Romaine
OTR1 Bags
  All samples were decayed, wet, and had an off-odor
  Final test day for OTR1 samples. OTR1 is not a good choice for baby romaine.
OTR2 bags
  Decay due to mechanical damage in some outer leaves
  Some rust spots in outer leaves
  Taste good; fresh. Leaves were crisp.

## Slide 15
Day 10 Green Leaf in Old OTR Bag – out of Carton
*Not pictured. Not opened due to not enough samples
Day 10 Green Leaf in Old OTR Bag – inside Carton
Day 10 Green Leaf in New OTR Bag – out of Carton
Day 10 Green Leaf in New OTR Bag – inside Carton

## Slide 16
Day 10 Baby Romaine in OTR1 Bag – out of Carton
Day 10 Baby Romaine in OTR1 Bag – inside Carton

## Slide 17
Day 10 Baby Romaine in OTR2 Bag – out of Carton
Day 10 Baby Romaine in OTR2 Bag – inside Carton

## Slide 18: Day 14
Green Leaf
New OTR Sleeves:
  Some mold present in outer leaves
  Minor rust spots
  Taste was good; fresh. Texture was crisp
Old OTR Sleeves:
  2 outer leaves had mold/mildew
  Taste was ok, but not as good as green leaf samples in New OTR sleeves
Baby Romaine – OTR 2 Bags
  Some samples had mechanical damage-related decay in the outer leaves
  3 leaves had rust spots
  Taste was good and texture was crisp

## Slide 19
Day 14 Green Leaf in Old OTR Bag – out of Carton
Day 14 Green Leaf in Old OTR Bag – inside Carton
Day 14 Green Leaf in New OTR Bag – out of Carton
Day 14 Green Leaf in New OTR Bag – inside Carton

## Slide 20
Day 14 Baby Romaine in OTR2 Bag – out of Carton
Day 14 Baby Romaine in OTR2 Bag – inside Carton

## Slide 21: Day 17
Green Leaf
New OTR Sleeves:
  Rust spots in 3 outer leaves
  Taste was good, sweet, and fresh. Texture was crisp.
Old OTR Sleeves:
  1 outer leaf had mold/mildew
  Rust spots were present in some outer leaves
  Taste was ok, but not as good as the green leaf in the new OTR sleeve
Baby Romaine – OTR 2 Bags
  Some samples were decayed and had an off-odor
  Mold present in 2 outer leaves
  Taste was good
  End of shelf life

## Slide 22
Day 17 Green Leaf in Old OTR Bag – out of Carton
Day 17 Green Leaf in Old OTR Bag – inside Carton
Day 17 Green Leaf in New OTR Bag – out of Carton
Day 17 Green Leaf in New OTR Bag – inside Carton

## Slide 23
Day 17 Baby Romaine in OTR2 Bag – out of Carton
Day 17 Baby Romaine in OTR2 Bag – inside Carton

## Slide 24: Day 20 Green Leaf
There was variability in all of the samples
New OTR Sleeves:
  1 outer leaf was decayed
  1 stem was decayed
  Taste was sweet, texture was crisp
Old OTR Sleeves:
  1 to 3 outer leaves had mold/decay
  Taste was ok, but not as good as the green leaf in the new OTR sleeve
Day 20 Green Leaf in Old OTR Bag – inside Carton
Day 20 Green Leaf in New OTR Bag – out of Carton

## Slide 25: Materials and Methods
Baby romaine and green leaf heads were grown and harvested on 1/28/19 at Springworks Farm at 70°F. The harvested product was moved to a cooler (34-36°F) and cooled for at least 30 minutes.
The harvested product was moved to a cooler (34-36°F). Baby romaine was packaged in Windham Packaging MAP bags (OTR 1 and OTR 2). Green leaf was packaged in sleeves with the original OTR from the previous study and sleeves with a new OTR (lower O2 flux rate). The product was packaged in the cooler and held at 34-36°F for 3 days.
The samples were packaged into vented, cooled cartons and transported to the laboratory at Windham Packaging, Windham, NH.
Packages were stored at 45-50°F for 4 days, then moved to 40-42°F for the remainder of the study.

## Slide 26: Procedures: Quality Testing
Weight was checked on days 0, 7, 10, 14, 17, and 20 using a digital scale
  Expressed as weight loss (%)
Quality observations such as decay, yellowing, mold/mildew, mechanical damage, stem color, browning, taste and off-odor were observed.
Temperature of lettuce was checked with an infrared thermometer while the product was both inside and outside of the bags.
Headspace readings inside packages were checked using a gas analyzer
Shelf life studies were done on each sample during each test day